## Slide 1: Introduction to Stairways and Ladders
1

## Slide 2: Introduction
Falls are the leading cause of fatalities in constructions
Falls from ladders make up about one-third of these fatalities
Approximately 25,000 injuries per year due to falls from stairways and ladders
Falls are preventable
Stairways and Ladders

## Slide 3: Types of Ladders & Stairways
Fixed ladders
Source: OSHA
Source: TEEX Harwood
Stairways and Ladders

## Slide 4: Types of Ladders & Stairways
Portable ladders
Source of photos: OSHA
Stairways and Ladders

## Slide 5: Types of Ladders & Stairways
Stairways
Source of graphics: OSHA
Stairways and Ladders

## Slide 6: Reducing or Eliminating Hazards
Ladder-use practices
  Extend side rails 3 feet above
the upper landing surface
  Don’t exceed load/capacity
  Use only as designed
  Angle ladder so the horizontal distance of bottom is ¼ the working length of the ladder
Source of graphics: OSHA
Stairways and Ladders

## Slide 7: Reducing or Eliminating Hazards
Pitch fixed ladders no more than 90 degrees from the horizontal
Avoid use of ladder on surfaces that are:
  Unstable
  Not level
  Slippery
Secure ladders to prevent movement
This ladder is not on a stable surface and is not properly positioned.
Source of photos: OSHA
Stairways and Ladders

## Slide 8: Reducing or Eliminating Hazards
Prevent movement/displacement
  Secure
  Barricade
Keep clear areas around top and bottom
Equally support rails of non-self-supporting ladder at the top
Source of photos: OSHA
Stairways and Ladders

## Slide 9: Stairways and Ladders
Ascending or descending ladder
  Maintain 3-point contact
  Face ladder
  Stay inside side rails
  Never carry tools/objects in hands
  Be extra careful getting on or off
Source: OSHA
Reducing or Eliminating Hazards
Source: OSHA

## Slide 10: Reducing or Eliminating Hazards
Don’t move, shift, or extend while in use
When exposed to energized electrical equipment, use nonconductive side rails
Don’t use the top two steps of a stepladder
Don’t climb the cross-bracing on the rear section of a stepladder
Source: TEEX – Harwood
Stairways and Ladders

## Slide 11: Stairways and Ladders
Remove defective ladders from service
  Broken or missing parts
  Corrosion
  Other faulty or defective components
Mark defective or tag “Do Not Use”
Repair to original design criteria
Source: OSHA
Reducing or Eliminating Hazards

## Slide 12: Reducing or Eliminating Hazards
Install handrail on stairways
  4 or more risers
  30 inches of rise
Source: OSHA
Stairways and Ladders

## Slide 13: Summary
Key components for ladder safety:
  A competent person must inspect
  Use the correct ladder for the job
  Use the correct angle, supports, treads, cross braces, and rails
  Don’t overload
  Your employer must train you in proper use of a ladder
Stairways and Ladders

## Slide 14: Summary
Key components for stairway safety
–Treads
  Rails
    Handrails
    Stair rails
    Guardrails
  Landings and Platforms
Stairways and Ladders

## Slide 15
Through the Alliance between OSHA’s 10 Regional Offices and the Elevator Contractors of America (ECA), Elevator Industry Work Preservation Fund (EIWPF), International Union of Elevator Constructors (IUEC), National Association of Elevator Contractors (NAEC), National Elevator Industry Educational Program (NEIEP), and National Elevator Industry Inc. (NEII), collectively known as The Elevator Industry Safety Partners, developed this Industry Specific Training for informational purposes only. It does not necessarily reflect the official views of OSHA or the U.S. Department of Labor. March 2025
Under the Occupational Safety and Health Act, employers are responsible (http://www.osha.gov/as/opa/worker/employer-responsibility.html) for providing a safe and healthy workplace and workers have rights (https://www.osha.gov/workers). OSHA can help answer questions or concerns from employers and workers. OSHA's On-Site Consultation Program (https://www.osha.gov/consultation) offers free and confidential advice to small and medium-sized businesses, with priority given to high-hazard worksites. For more information, contact your regional or area OSHA office (https://www.osha.gov/contactus/bystate), call 1-800-321-OSHA (6742), or visit https://www.osha.gov/.